## Slide 1: Direct Drive Electric Scooter
Goal
Design and develop a Direct Drive
Electric Scooter as an alternative
form of urban transportation.
Specifications
Use a BLDC motor, Golden Gate Motor Controller from previous “E-Bike” project along with 40 Cells.
Implement a “boost feature” Using Current Feedback and creating an profile.
Integrate current signal to estimate remaining battery charge.
  Supervisor - Dr. Paul Gaynor
  Student - Matt Kokshoorn

## Slide 2: System Overview
User Control:
Throttle
Break
Boost
μContoller:
Over Current Management.
Motor Speed Controller
LCD Display:
Remaining Battery.
Motor Speed.
Throttle
Signal
BLDC
Motor
Speed Signal
Current Transducer Board
Supply
Current Signal

## Slide 3: Mechanical & Electrical Design

## Slide 4: Signal Conditioning
Normal Control Strategy
1st Order RC Filter
2nd Order Sallen-Key Filter
Throttle Input
Current Board ()
Current Signal Feedback

## Slide 5: Overcurrent Algorithm
Basis - Can run motor at twice the rated current for 60 seconds when boost is activated.
Note: is also used
for remaining charge calculation.
Initilise product to zero
millisecond interrupt
Measure Current
Add Difference to product
Calculate Instantaneous Product
Exceeded ?
NO
YES
Disable Overcurrent by Reducing Output Speed Signal
Re-enable Overcurrent if
<

## Slide 6: Demonstration Set-up Values
  In standard operation the motor rating are,
  - 400W Rated Power (15.15A at 26.4V).
  - 800W Peak Power (30.3A at 26.4V).
  Capable of 60 seconds of peak power
  i.e. An product limit of 38640
  For the purpose of this demonstration:
  - 92.4W Rated Power (3.5A at 26.4V).
  - 184.8W Peak Power (7A at 26.4V).
  Capable of 10 seconds of peak power
  i.e. An product limit of
Motor Specifications
Supply
8 series sets of 5 Parallel giving,
26.4V
11.5 Ahr
303.6 Whr.

## Slide 7: Speed Waveform

## Slide 8: Motor Current Waveform (No Load)
Chart: Time (s)

## Slide 9: Motor Current Waveform (Loaded)
Chart: Time (s)
Current Control Parameters:
-
-

## Slide 10: Encountered Problems & Solutions
Regenerative breaking not working -> Pull down resistor added.
Throttle malfunction -> Hall Effect sensor replaced.
Unstable Current Limiting -> PID Controller.
Future Work
Insulation and Protection.
Regenerative Breaking Current Testing.
Charging Connection.
Optimization of PID Gains.
Increased Acceleration.
Acknowledgements:
Dave Healy (Mechanical Fabrication).
Ken Smart (Workshop Assistance / Mechanical Load).